## Slide 1: Series and Parallel circuits

## Slide 2: Series and parallel circuits
Learning objectives
Distinguish between series and parallel circuits
State that ammeters are placed in series
Predict the current at different points in a circuit

## Slide 3: Series Circuit
All the components are in the same loop
Adding bulbs increases the resistance
Increasing the resistance lowers the current
A lower current results in dim bulbs

## Slide 4: Parallel Circuit
The bulbs are in a separate loop
Adding bulbs does not increase the resistance
The current through both bulbs is not lowered
Both bulbs are bright
A1
A2
A3
A1 = A2 + A3

## Slide 5: Two-way switches
Two-way switches allow us to turn a light on or off from both the top and bottom of a stairway.

## Slide 6: Two-way switches
Moving the switch at either the top or the bottom of the stairway will turn off the light.
Turning the switch on at the bottom will turn on the light. On reaching the top of the stairs, the light can be turned off without returning to the bottom of the stairs

## Slide 7: Voltage and resistance

## Slide 8: Voltage and resistance
Learning objectives
Use voltmeters to determine the voltage across components in a circuit
Control the brightness of a bulb using a variable resistor (Rheostat)

## Slide 9: Voltage
V1
V3
V2
Conclusion
Voltmeters are placed in parallel
V1 = V2 + V3
The voltage provided by the battery or power pack is shared across the components in series

## Slide 10: Resistance
Conclusion
A variable resistor consists of a long coiled wire. The wire has a resistance and the greater the length of the wire the greater the resistance.